## Slide 1: Test 1
Covers lecture and text material through Chapter 9.
Sunday (Oct. 15th) by 1:00 P.M. EST, I will email the exam to your maine.edu email account.
There will be no class on Tuesday (Oct. 17th), but I will be in my office from 7:30-10:30 to answer any questions.
Completed exams are to be emailed to me, no later than 8:00 P.M. EST, on Tuesday, October 17, 2017.

## Slide 2: Labs
Lab 2 will be returned later today or first thing tomorrow.
Lab 4 will be posted on Tuesday, due Tuesday, Oct. 24.

## Slide 3: Getting Data Into Your GIS Project
Lecture 10
End of Chapter 9 & Chapter 10 to page 460.

## Slide 4: Adding Excel Tables
Be sure to save as a 1997-2003 Excel workbook.

## Slide 5
Tables can then be joined or related to a feature attribute table using a common attribute.

## Slide 6: Adding X,Y Data

## Slide 7: Geocoding
The Process of assigning locations to addresses so that they can be placed as points on a map.
Also called “address matching”.
The process assigns geographic coordinates to the original data.
Required: two tables
  A reference table containing street segments with address ranges.
  A table with street addresses and a city/zip code.

## Slide 10
Misspelled
Incorrect Suffix
Add both tables to ArcMap.
Not really in Bangor

## Slide 18: How Does Geocoding Work?
Starting from the downtown.
Addresses run even on left side of street.
Odd on the right side.

## Slide 19
Segment length: 300 feet
Find the location of 330 Schaffer Hills Drive.

## Slide 20: The Joys and Sorrows of Geocoding
IRINA GALKINA
PROFESSOR CONSTANCE C. HOLDEN
SIE 509
DECEMBER 15, 2011

## Slide 21: Geocoding White Pages Directories
How does it work?
How accurate is it?
How can it be used in different applica-tion settings?
Data provided by Maine Office of GIS

## Slide 22: Work flow
Address Locator
Table of Addresses
E911 Roads File
obtaining data
preparing data
creating address locator
ge0coding
evaluating the results

## Slide 23: Offset Distance
Will work
Will not work
10 Sylvan Road
1 Sylvan Road

## Slide 24: First Attempt

## Slide 25: Failure to Match
errors in the address recording process
errors in the street segment data

## Slide 26: Errors in the Address Recording Process
Blank Addresses:
2. Incomplete Address:
3. Spelling or Formatting mistakes:
Inconsistencies between the address data and the street data file:
Address table: Newman Ln, Crestview Ln, Penobscot St.
E911 mapbook: Newman Rd, Crestview Rd, Penobscot Dr.

## Slide 27: Errors in the Address Recording Process
Disagreement between the common name of a location and the official address:
Apartment complexes names instead of street names: Talmar Woods, Hasbrouck Court
Typos: 1952 Park Street?

## Slide 28: Errors in the Reference Data
1. Incomplete,
or erroneous
street ranges:
Missing street ranges:
30/51/35 Merritt Drive
7 Colburn Drive?

## Slide 29: Error in the Reference Data
3. Missing street segments:
100/106
Penobscot St?
72 Penobscot St

## Slide 30: No street with the name given?
10 records with Hill for the street name?
Final decision:
Treats Fall House,
2 Hillside Road

## Slide 31: Rematching
Automatic
Lower spelling sensitivity
Match to candidates in reasonable proximity
Use the Pick Address from the Map
2 Timberview Drive
the ODD side of the street!

## Slide 33: Analyzing Matched Addresses

## Slide 34: How does digital orthophotography help?
Misaligned?
Properly aligned!

## Slide 35
2
4
6
8
9
7
5
3
1
2
4
6
8
House Numbers on the Parcel Layer vs. Geocoded Results
Geocoded Address Points:
Issues with Spatial Interpolation

## Slide 36
Issues with Spatial Interpolation
79
77
75
69
65
63

## Slide 37: Errors in the Reference Data
Winterhaven Left: 1 – 27
Right 2 – 96

## Slide 38: Editing
Offset is not an option.
Moving points manually in editing mode
BEFORE
AFTER

## Slide 39
The match score of 95 % says nothing about the quality of results.
A Table of 83 unmatched addresses sums up possible reasons for geocoding failure.
Are there any better alternatives?
RESULTS
Geocoding to tax parcel layer
Rooftop geocoding
Geocoding to street centerline

## Slide 40: Spatial Analysis Part 3
Chapter 10 Raster Analysis – Part 1

## Slide 41
Raster Data Model
Raster cells store data (nominal, ordinal, interval/ratio)
Forest
1,…9,10
259.63
Excellent for terrain and hydrological modeling
Complex constructs built from raster data
  -Connected cells can be formed in to networks
  -Related cells can be grouped into neighborhoods or regions

## Slide 42: Examples of Raster Analysis
Predict fate of pollutants in the atmosphere
The spread of disease
Animal migrations
Crop yields
EPA - hazard analysis of urban superfund
sites
Market analysis
Watershed analysis
Terrain analysis

## Slide 44
Map algebra
Concept introduced and developed by Dana Tomlin and Joseph Berry (1970’s)
Cell by Cell combination of raster data layers
  -Each number represents a value at a raster cell location
  -Simple operations can be applied to each number
  -Raster layers may be combined through operations such as addition, subtraction and multiplication

## Slide 46
Incompatible cell sizes and boundaries confound multi-layer raster analysis.
Notes: Incompatible cell sized and boundaries can cause problems with multi-layer raster operations. What cell value would you choose from layer 2 to combine with layer 1n and a portion of cell B is undefined.
Ambiguities are best resolved by resampling prior to layer combination

## Slide 47
Scope: Local operations
Notes: As with vector analysis, the scope of raster analysis can be classified as local , neighborhood or global

## Slide 48: Many Local Functions
(page 448 of text)
Apply to interval/ratio data.

## Slide 49: Logical Operations AND
Non-zero values are “true”, zero values are “false”
N = null values

## Slide 50: Logical Operations OR
Non-zero values are “true”, zero values are “false”
N = null values

## Slide 51: Logical Operations NOT

## Slide 52
More Local Functions – logical comparisons

## Slide 53: An Example of a Logical Operation

## Slide 54: Reclassification
Notes: Raster reclassification assigns output values that depend on a specific st of input values.

## Slide 55
Conditional
Function

## Slide 56
Nested Functions

## Slide 57
Raster Overlay
Typically applied to nominal or ordinal data
Cell by cell process which results in the combination of the two input layers
Pay attention to the number of possible combinations that may be possible and understand the effect on the output layer

## Slide 58
Feature numbers increase in overlay

## Slide 59: Overlay
Notes: Many differences between vector and raster overlay due to differences in the data models. Raster overlay is often restricted to nominal data. Overlay with continuous data creates to many unique cell combinations to be of much use,

## Slide 60: Raster Clip Operation
Notes: The output layer includes only source values indicated by the output layer.

## Slide 61: Raster Addition

## Slide 62: Be Careful of Ambiguity

## Slide 63
A raster clip operation preformed by multiplication of a binary mask.

## Slide 64: Raster Overlay in Idrisi

## Slide 65
1 | 0 | 1
1 | 0 | 1
1 | 0 | 1
1 | 1 | 1
0 | 0 | 1
0 | 0 | 1
1 | 0 | 1
0 | 0 | 1
0 | 0 | 1
First * Second
0*0=0
0*1=0
1*1=1

## Slide 66
1 | 0 | 1
1 | 0 | 1
1 | 0 | 1
1 | 1 | 1
0 | 0 | 1
0 | 0 | 1
2 | 1 | 2
1 | 0 | 2
1 | 0 | 2
First + Second
0+0=0
0+1=1
1+1=2